## Slide 1: Approximation Wave Propagation with Runge-Kutta Method in One Dimension
Xintong Wang 7731912
Jiayi Sun 9307901
Xi Sun 496474

## Slide 2: Motivation
What is wave propagation?
Our project will emphasize on ocean waves.
  Design of the floodbank
    The height of possible incoming tsunami
  Design of the dam
    The pressure applied on the dam
The difficulty of tracking ocean wave profile
  The detector can only access the speed and the direction of the ocean waves
  Data points

## Slide 3: Problem Statement
The speed and direction of the ocean waves is essentially the derivative of the wave profile.
We know ut(x,t) which is the speed of waves at time t at location x.
We want to find the value of u(x,t) for a given x and for any t.
  This value represents the height of the ocean wave at the location x at the time t.
  It will provide us information about how strong our floodbank needs to be in order to withstand the impact of tsunamis

## Slide 4: Method :Runge-Kutta Method
Why Runge-Kutta?
  Runge-Kutta methods have the high-order local truncation error than Taylor methods but eliminate the need to compute and evaluate the derivatives of u(x,t), which is unknown for us.
  Although it is slower, but it gives more accurate answers. Here, the accuracy is crucial.
How to implement and solve?
  Plug points of ut(x,t) with fixed x into python function Runge-Kutta Method to find corresponding value of u(x,t).
  How to validate?
    Compare with previous project in 104A, which employed Natural Cubic Spline method.

## Slide 5: Results
Location | Time t | Approximation | Actual Value | Absolute Error
x=0 | 1 | -7.063069965 | -7.0605434589 | 0.00252650672021
 | 2 | -7.632385977 | -7.6296558231 | 0.00273015481344
 | 3 | -1.184521520 | -1.1840978094 | 4.23711161948e-04
 | 4 | 6.3523865600 | 6.3501142694 | 0.00227229057779
 | 5 | 8.048939732 | 8.04606057410 | 0.00287915883952
 | 6 | 2.34533483495 | 2.344495893 | 8.38941742112e-04
The maximum height of the waves are 8.048939732 meters with error less than 0.01m=1cm. The height of floodbank we need is at least 9 meters above the sea level.